## Slide 1: RDS / RDSadmin Architecture, System, Program & Screen Shot
Jacky Lue
2016/03/11

## Slide 2: Content
Architecture Background
System Concept
Program Overview
RDS Program
RDS-admin Program

## Slide 3: Architecture Background

## Slide 4: SPA….. You are not alone !
Home Network
Internet,
Cloud
Peripheral Devices
SPA

## Slide 5: Connections in New-SPA architecture
Internet
  Purpose: Remote access
  Connect to/from: mobile App, homepage,…
Home network
  Purpose: Home Automation
  Connect to/from: TV, Phone, IPCAM, Thermostat,…
Device Local network
  Purpose: Internal ctrl/data
  Reserve expand capability for New-SPA Adding new device to enhance User experience

## Slide 6: New SPA External Architecture
Internet , Public cloud, Private cloud….
Web Server
Application Server
Wireless connecting Peripheral Devices
Local Database
Big data
Database
SPA Company
Call-center
Internet/cloud Company
Local Network
Home Network

## Slide 7: System concept

## Slide 8: High Level Concept on RDS
Original start point :
Reduce communication time in call-center
Take right parts when on-site service (go to user-Home)
Add-on (with Cloud)
Analysis user behavior (for future product planning)
Provide add-on service
Push new product information

## Slide 9: Through internet, SPA company could reach user machine directly
Internet
Web Server
Cloud
Data Base SQL-server
intranet
Application Server
Call-center
User in Home
User out of Home
SPA company
1 to many, always
1 to 1, when control/diagnosis

## Slide 10: Architecture of RDS
Customer
Information
Customer Database
Machine
Logging
Database
Connect
&
Diagnosis
Polling /Logging
Every Machine
And Analysis
消耗品紀錄
購買紀錄
 Remind !
Push
Information
50K ~ 500K machines
Only one
machine
Machine ID
Web-site
Homepage
Mobile
App
Call-center
User
SPA connected
Not connected
Simple version RDS
Server version RDS

## Slide 11: What we provide?
Past:
  Mobile App for SPA control
Current Stage:
  Mobile App
  RDS (with NAS) for call-center
Future:
  Mobile App
  RDS (server ver.) for call-center
  Active services…

## Slide 12: Program overview

## Slide 13: Scenario (1/2) Inside Call-Center
Call-center operators
RDS program
Call-center
Manager
RDS admin program
NAS
Storage

## Slide 14: Scenario (2/2) Database Integration
SPA Company /dealer
Service Database
SPA Company /dealer
Customer Database
MIS

## Slide 15: Overview (current version)
Two program
  RDS for call center operators
  RDS-admin for manager
Work with NAS as center storage (not work with center database)
  Account
  RDS report:
    save by UID
    save by Date
  Operation record (by RDS accounts)
  Open service call

## Slide 16
Original discussion at 2016-Jan, by Thomas, Jacky, Judy.

## Slide 17: Directories in NAS
Z:\RDS system root directory
Z:\RDS\RPT report root directory
Z:\RDS\RPT\UID report saved by UID
Z:\RDS\RPT\DATE report saved by Date
Z:\OSC current open service call
Z:\OSC\cDATE closed service call
Z:\LOG\UID operation record (by UID)

## Slide 18: Files Create & Delete in NAS
Call-center operators
RDS program
NAS
Storage
Company
Service DB
Company
Customer DB
MIS
Create
Only!
Process then Delete !

## Slide 19: RDS program

## Slide 20: RDS (1) : Login

## Slide 21: RDS (2) : Main
Input UID
If connect ion fail…

## Slide 22: RDS (3) : Connected
If this UID
had connecting history,
Auto-shows basic Info.
Auto-show information
Related to current Error
High-end model
Low-end model
Auto detect & show..

## Slide 23: RDS (4) : Change Filter Schedule
High-end Model
When ECO is off
When ECO is on

## Slide 24: RDS (5) : Change Filter Schedule
Low-end Model

## Slide 25: RDS (6) : Change Date/Time

## Slide 26: RDS (7) : Dynamic Show Error Info.
Green color:
Message, not Error
Red color: Error
Newly display
two part of info. (LOKP. FSO)

## Slide 27: RDS(8): Error Messages
Take some time to get
max 50 recorded Errors
Which stored in SPA
Current Error
Don’t has End Time

## Slide 28: RDS(9) Auto-Diagnosis Start
Press Button,
Will Light-on when doing Auto Diagnosis
Auto-Diagnosis messages
And if errors changed message (ORG.= LOKP,FSO)

## Slide 29: RDS(10) Auto-Diagnosis Finished
After finished,
The button will Light-On
Auto-Diagnosis finished message

## Slide 30: RDS(11) Produce Service Call No.
After it produced.
The button will Light-On
Press Button, Service Call Info. show here

## Slide 31: RDS(12) SC No. Encoding
UID = DLCT2SZP6WUAUNPPMX6J
Report 編碼原則: UID號碼 + 日期(月日年) + 此用戶在當天的第幾筆連線,
Example: FVC91WZP6JAUVN6PMXKJ_012816_3
工單編碼: Report 編碼 + P(哪位操作員)+S (今天第幾筆工單), Example: FVC91WZP6JAUVN6PMXKJ_012816_1_P1S2
每一個Report 都有編碼
但不是每一個Report都有編碼 +工單號碼
需要工單的 Report 會有Report編碼 + 工單號碼
PS: P0 = Supervisor
工單 and RDS Report是同一份文件檔案
Example: FVC91WZP6JAUVN6PMXKJ_012816_1_P1S2.csv
Operation record (Log)所存檔案名稱也是相同編碼,
有可能有 Log 卻沒有 RDS report
Example: FVC91WZP6JAUVN6PMXKJ_012816_3.log

## Slide 32: RDS(13) Produce RDS Report
After it produced.
The button will Light-On
Press Button,
Report show in new Form.

## Slide 33: RDS(14) Printing RDS Report
Press Button,
Printer Dialog will show
(Just like Windows Application)

## Slide 34: RDS(15) Clear All When Dis-connect

## Slide 35: RDS(16) History of this UID
Only UID input required, Even didn’t connected,
You could press “History” button to check history of past

## Slide 36: RDS(17) Check History when A.D
Even you are waiting Auto-Diagnosis
You could press “History” button
Could check
RDS full report

## Slide 37: RDS(18) My Open Service Call List
Only log-in required, Even didn’t connected and No UID inputted,
You could press “My S.C. List” button to browser your open service call list
Could input
Replaced parts
& comment
Then save it
& delete this SC

## Slide 38: RDS(19) Close a Service Call
Press Button
& confirm it…

## Slide 39: RDS(20) Check the closed Report
Use UID to see history, then it already changed
Notice that, file already deleted in OSC dir.
And the updated file already copy to both:
\RDS\RPT\UID\xxxx\xxxxxxx…xx
\RDS\OSC\cDATE\2016/02/25

## Slide 40: RDS(21) Report Files
0224
0224
0224
\RPT\UID\xxx…
\RPT\DATE\2016\02\24\
\OSC\
When 2/24, a service call submitted. Three file saved
0224
0224
\RPT\UID\xxx…
\RPT\DATE\2016\02\24\
\OSC\
When 2/25, a service call closed. Update 1 file, Delete 1 file and Add 1 file.
0224
\OSC\cDATE\2016\02\25

## Slide 41: RDS(22) Operation Records

## Slide 42: Process of Auto-Diagnosis
設定un-lock, 設定 STD mode, 設定filter schedule讓當下時間不是循環時段, 並且記住原來的設定水溫, 原來的STD/ECO mode, 原來的filter schedule
如果SPA正在加熱, (會看到 Heater + Circ + UV all on) 則先進行(3)(4), 再進行(5), 然後(8)結束 如果SPA沒有在加熱, (Heater + Circ + UV all off), 則先進行(5), 再進行(6)(7), 然後(8)結束 如果SPA正在加熱, (會看到 Heater + Circ + UV all on) 但目前水溫過低 則直接進行(5), 然後(8)結束
關掉所有pump/blower, 量測電流 (heater+循環)
讓設定溫度比水溫低2度F, 量測電流 (循環only), 再一分鐘等待循環結束
關掉所有pump/blower, 再依序單獨開各個pump/blower 量測電流
讓設定溫度比水溫高2度F, 量測電流 (循環only)
等一分鐘,(heater on), 量測電流 (heater+循環)
回復原來的設定,結束.

## Slide 43: Note: Total time of A.D.(1)
>>>>>>>>>>>>>>>>>>>>>>>>
Auto-Diagnosis starts...
22:45:25> ---- S_idel ---
22:45:25> to C_std
22:45:29> to S_saveFsch
>> Save current setting...
22:45:29> to C_saveFsch
22:45:33> to S_setFsch
>> Save current filter schedule...
22:45:33> to C_setFsch
>> Trun of all pump & blower...
22:45:41> to S0_all_off
22:45:41> to C0_all_off
22:45:45> C0_all_off
22:45:51> M0_all_off
>> all off : 0A (Normal)
22:45:51> S1_P1_hi
22:45:55> C1_P1_hi
22:45:55> S1_P1_hi
22:45:59> C1_P1_hi
22:45:59> S1_P1_hi
22:46:03> C1_P1_hi
22:46:09> M1_P1_hi
>> Pump-1 Hi + Circ + UV : 7A (Normal)
22:46:09> S2_P1_lo
22:46:12> C2_P1_lo
22:46:18> M2_P1_lo
>> Pump-1 Lo + Circ + UV : 3A (Normal)
22:46:18> S3_P2_hi
22:46:22> C3_P2_hi
22:46:22> S3_P2_hi
22:46:26> C3_P2_hi
22:46:32> M3_P2_hi
>> Pump-2 Hi : 12A (Normal)
22:46:32> S7_blower
22:46:36> C7_blower
22:46:42> M7_blower
>> Blower : 0A (Normal)
>> Trun on circuration...
22:46:56> M_HeatOn_CircOnly
>> CP + UV : 1A (Normal)
22:47:00> W_HeatON_CircOn
22:47:04> W_HeatON_CircOn
22:47:08> W_HeatON_CircOn
22:47:12> W_HeatON_CircOn
22:47:16> W_HeatON_CircOn
22:47:20> W_HeatON_CircOn
22:47:25> W_HeatON_CircOn
22:47:29> W_HeatON_CircOn
22:47:33> W_HeatON_CircOn
22:47:37> W_HeatON_CircOn
22:47:41> W_HeatON_CircOn
22:47:45> W_HeatON_CircOn
22:47:49> W_HeatON_CircOn
>> Trun on heater...
22:47:55> M_HeatOn_CircOn
>> Heater + CP + UV : 21A (Normal)
>> Restoring original setting...
22:47:55> S_Over
22:47:59> C_Over
22:47:59> S_Over_SetT, setT as 69
22:48:03> C_Over_SetT
>> Restoring original filter schedule...
22:48:03> S_bkFsch
22:48:11> C_bkFsch
>>>>>>>>>>>>>>>>>>>>>>>>>>>> finished
Case: Heater-off & Circ+UV off
With following setting
3 min 左右

## Slide 44: Note: Total time of A.D.(2)
>>>>>>>>>>>>>>>>>>>>>>>>
Auto-Diagnosis starts...
23:05:44> ---- S_idel ---
23:05:44> to C_std
23:05:47> to S_saveFsch
>> Save current setting...
23:05:47> to C_saveFsch
23:05:51> to S_setFsch
>> Save current filter schedule...
23:05:51> to C_setFsch
>> Trun of all pump & blower...
23:05:59> to S_HC_all_off
23:05:59> to C_HC_all_off
23:06:03> C_HC_all_off
23:06:09> M_HC_all_off,
>> Heater + CP + UV : 21A (Normal)
>> Turn off heater...
23:06:09> S_HeatOff, curWaterT=72
23:06:13> C_HeatOff
23:06:23> M_HeatOff_CircOnly
>> CP + UV : 1A (Normal)
>> Waiting Circuration off...
23:06:27> W_CircOff
23:06:31> W_CircOff
23:06:35> W_CircOff
23:06:39> W_CircOff
23:06:43> W_CircOff
23:06:47> W_CircOff
23:06:51> W_CircOff
23:06:56> W_CircOff
23:07:00> W_CircOff
23:07:04> W_CircOff
23:07:08> W_CircOff
23:07:12> W_CircOff
23:07:12> to C0_all_off
23:07:16> C0_all_off
23:07:22> M0_all_off
>> all off : 0A (Normal)
23:07:22> S1_P1_hi
23:07:26> C1_P1_hi
23:07:33> M1_P1_hi
>> Pump-1 Hi + Circ + UV : 7A (Normal)
23:07:33> S2_P1_lo
23:07:37> C2_P1_lo
23:07:43> M2_P1_lo
>> Pump-1 Lo + Circ + UV : 3A (Normal)
23:07:43> S3_P2_hi
23:07:47> C3_P2_hi
23:07:53> M3_P2_hi
>> Pump-2 Hi : 11A (Normal)
23:07:53> S7_blower
23:07:57> C7_blower
23:08:03> M7_blower
>> Blower : 0A (Normal)
>>Restoring original setting...
23:08:03> S_Over
23:08:07> C_Over
23:08:07> S_Over_SetT, setT as 73
23:08:11> C_Over_SetT
>> Restoring original filter schedule...
23:08:11> S_bkFsch
23:08:19> C_bkFsch
>>>>>>>>>>>>>>>>>>>>>>>>>>>> finished
Case: Heater-off & Circ+UV On
With following setting
3 min 左右

## Slide 45: Error code and Auto-Diagnosis
Error Codes |  | Definition | Can do Auto Diagnosis ? | Possible Result | 
Old | New |  |  | if happen | then it's….
WSO | SN1 | Water temperature sensor OPEN | Y |  | 
WSS | SN2 | Water temperature sensor SHORT | Y |  | 
HSO | SN3 | Hi-Limit temperature sensor OPEN | Y |  | 
HSS | SN4 | Hi-Limit temperature sensor SHORT | Y |  | 
PSO | SN5 | PCB temperature sensor OPEN | Y |  | 
PSS | SN6 | PCB temperature sensor SHORT | Y |  | 
LOKA | L1 | Panel Locked. All functions locked. | Y |  | 
LOKP | L2 | Pump locked. | Y |  | 
LOKE | L3 | Temperature locked. | Y |  | 
LOKS | L4 | Service locked. for 120 minutes | Y |  | 
FSO | FL1 | Flow switch OPEN | Y |  | 
FSC | FL2 | Flow switch CLOSE | Y |  | 
FSC1 | FLO2 | Flow switch CLOSE - 1 | N |  | 
R1 | .. | Pump 1 high speed relay fuse | N |  | 
R2 | .. | Pump 2 high speed relay fuse | N |  | 
R3 | .. | Pump 3 high speed relay fuse | N |  | 
RH | .. | Heater relay fuse | N |  | 
WHO | OH | Water is over heated | Y |  | 
WCL | COOL | Water is cool | Y |  | 
WICE | ICE | Water is too cold | Y |  | 
WWD | WWD | Water is too hot | N |  | 
CBB | BLB | UV light usage expired | Y |  | 
FEX | CF | Filter usage expired | Y |  | 
PCBH | HOT | PCB Temperature exceeds 180F | Y |  | 

## Slide 46: Possible Cause & Equipment
code (8 bit) | from | Cause | Equpipments | comment
0 |  | None. (Reserved for empty) | None | 
1 | Err1234 | Water temperature sensor defect | Water temperature sensor | 
2 | Err1234 | Hi-limit temperature sensor defect | Hi-limit temperature sensor | 
3 | Err1234 | Circ Pump defect | Circ Pump | 
4 | Err1234 | Fuse on board defect | Fuse | 
5 | Err1234 | Pipe Blockage | Pipe | 
6 | Err1234 | Dirty Filter | Filter cartridge | same as 9
7 | Err1234 | Flow Switch defect | Flow Switch | FSO , during AD measureent
8 | Err1234 | UV light usage expired | UV light | 
9 | Err1234 | Filter Cartridge expired | Filter Cartridge | same as 6, use 6
10 | Err1234 | Board defect | Board | 
11 | Err1234 | Topside defect | Topside | 
12 | A.D. | Pump-1 Hi (line) defect | Pump-1 Hi | 
13 | A.D. | Pump-1 Lo (line) defect | Pump-1 Lo | 
14 | A.D. | Pump-2 Hi (line) defect | Pump-2 Hi | 
15 | A.D. | Pump-2 Lo (line) defect | Pump-2 Lo | 
16 | A.D. | Pump-3 Hi (line) defect | Pump-3 Hi | 
17 | A.D. | Pump-3 Lo (line) defect | Pump-3_Lo | 
18 | A.D. | Blower (line) defect | Blower | 
19 | A.D. | Circ Pump + UV (line) defect | Circ Pump + UV light | 
20 | A.D. | Heater (line) defect | Heater | 

## Slide 47: RDS Related System File
In RDS root directory Z:\RDS\
User.ini  RDS user accounts
In open service call Dir. Z:\OSC\
[1,2,…].work
 keep last SC number
 by each operator

## Slide 48: RDS-admin program

## Slide 49: RDS admin(1) Login

## Slide 50: RDS admin (2) mainly show Open Service Call List

## Slide 51: RDS admin (3) check it’s brief report
Click
Double
Click

## Slide 52: RDS admin (4) Menu buttons

## Slide 53: RDS admin (5) Supervisor Account
Just show information….
Can be edit and Save…

## Slide 54: RDS admin (6) User List
Click
Double Click

## Slide 55: RDS admin (7) RDS Full Report

## Slide 56: RDS-admin Related System File
In RDS root directory
System.ini  Supervisor account
User.ini  RDS user accounts

## Slide 57: Back-Up

## Slide 58: Some Error Can Not Do Auto-Diagnosis
In following Error case, user can not do auto-diagnosis:
WWD
FSC1
R1
R2
R3
RH

## Slide 59: If lose connection when service…

## Slide 60: A.D. Example: Heat off & Circ. off

## Slide 61: A.D. Example: Heat on & Circ. on

## Slide 62: No Spa-Serial & Model-Name Cannot do RDS Report